Raspberry Pi Projects
- for your home -

---
Overview
- Weather station
- Heatpump hack
- Garage door opener

---
Raspberry Weather
https://www.raspberryweather.com/

---
Raspberry Weather (2)
- Necessary parts
  - RPi B
  - Adafruit Pi cobbler breakout kit
  - Breadboard wire bundle
  - Full sized breadboard
  - DHT22 or DS18B20 sensor
  - Wifi dongle (if necessary)
https://www.raspberryweather.com/necessary-parts/

---
Raspberry Weather (3)
- Sensors
  - DHT22: temperature and humidity but not very reliable
  - DS18B20: reliable, waterproof, but no humidity
  https://www.raspberryweather.com/which-sensor-to-buy/

---
Raspberry Pi (4)
- Software stack
  - Apache/nginx
  - Wordpress
  - Python (for accessing sensors)
- Optional
  - Android app (id=com.raspberryweather)

---
Hacking your heatpump
- Well, Mitsubishi ones at least
- Tutorial
  https://nicegear.co.nz/blog/hacking-a-mitsubishi-heat-pump-air-conditioner/
- Code
  https://github.com/hadleyrich/MQMitsi

---
Hacking your heatpump (2)
- Communication port CN105
- 5V TTL UART @ 2400 bps and even parity

---
Hacking your heatpump (3)
heatpump
Control interface
RPi breakout board

---
Garage door opener
- Found at instructables
  http://www.instructables.com/id/Raspberry-Pi-Garage-Door-Opener/
- Overview